## Slide 2
4 channel vs 2 channel detection
2 channel detection can cause sequencing errors due to phasing issues
and can cause polyG tracts at the end of fragments
MiSeq, HiSeq 4000 and X
MiniSeq, NextSeq, NovaSeq

## Slide 3
Patterned flow cells
Improves regularity of densities and qualities
Reduces analysis time

## Slide 4
Sequencing qualities
Intensities
Cluster densities
Density of clusters for each tile in thousands/mm2. Overloading of the library may cause merging of clusters, lowering of the % PF and reduction of the quality score (Q30)
Intensity values of the four incorporated bases are measured to determine if a clustering failure has occurred
Reflects the purity of the signal from each cluster. Ratio of the brightest intensity divided by the sum of the brightest and second brightest intensities for each cycle. Optimal values for MiSeq and HiSeq 2500 from 80-95%.
Percentage of reads passing filter (% PF)
Underclustered Overclustered

## Slide 5
Sequencing qualities
Phasing/Prephasing
Percentages of bases that fell behind or jumped ahead the current cycle within a read. It increases with cycle number, hampering correct base identification for long reads. Optimal values are below 0.5 or 0.2% depending on platform. Issues may arise when read length is above specifications.
% Q-score > 30 : percentage of bases that have a a probability of incorrect base calling of 1/1000. Low Q scores can increase false-positive variant calls, which can result in inaccurate conclusions.
Q-score
Base calling error probabilities P : Q = − 10 log10 P

## Slide 6
Sequencing qualities
Percentage of alignment
Error rate
% align: percentage of the reads aligned to PhiX control genome. It is important to estimate the error rate. Indication on the success of the clustering process.
Calculated for each read based on the aligned % of PhiX control sample. Important to determine if the sequencing has proceeded as expected.
Error rate ≈ 0.1 %
“bad” sequencing

## Slide 7: Many applications

## Slide 8
  SINGLE CELL TECHNOLOGIES
Most widely used device to study single-cell transcriptomics : Chromium controller (10x Genomics)
Several applications :
Single cell Gene expression
Measures gene activity on a cell-by-cell basis, characterize cell populations, cell types, …
Linked read genomics
Performs diploid de novo assembly, phase haplotypes, genetic variations
Single cell ATAC
Measures epigenetics by detecting open chromatin regions
Single cell transcriptomics allows to study transcriptome heterogeneity,
to investigate differences in transcript expression and gene regulation in individual cells :
  Differences in trancript abundance
  Alternative splicing and differential expression of isoforms

## Slide 10
CHROMIUM SINGLE-CELL RNA SEQUENCING
3’
5’
barcodes separately index
each cell’s transcriptome
Single cells undergo RT
All cDNAs from one cell
share the same barcode
barcoded sequencing library

## Slide 11
CHROMIUM SINGLE-CELL RNA SEQUENCING
DATA ANALYSES
CELL RANGER :
Chromium data
analysis pipelines

## Slide 13
acquisition of U.S. company Complete Genomics in 2013
NEW SEQUENCING TECHNOLOGY

## Slide 14
NEW SEQUENCING TECHNOLOGY

## Slide 15
  PART 2
  3rd GENERATION SEQUENCING
  LONG READS

## Slide 16
LONG-READS VERSUS SHORT-READS
NGS short reads assembly
Long reads assembly
Assembly of DNA fragments with repeated sequences
Several contigs incomplete assembly, underestimation of repeats

## Slide 17
LONG-READS VERSUS SHORT-READS
Haplotype phasing
T
G
T
G
T
G

## Slide 18
LONG-READS VERSUS SHORT-READS
Detection of splicing isoforms

## Slide 19
MinION - Oxford Nanopore
Single molecules
> 200 000 bp long
Error rate ≈ 10-15 %
Compensated by coverage
The 3rd generation
winning technologies
Sequel - Pacific Biosciences
Single molecules
Up to 80,000 bp long
Error rate ≈ 10-15 % - CCS: <1%
Compensated by coverage

## Slide 20
PacBio DNA-seq library
PacBio : Single Molecule Real Time (SMRT) sequencing

## Slide 21
ZMW
Pacific Biosciences

## Slide 22
Pacific Biosciences
ZMW : optical waveguide that guides light energy into a volume that is small compared to the wavelength of the light

## Slide 23
Pacific Biosciences

## Slide 24
Pacific Biosciences

## Slide 25
Pacific Biosciences

## Slide 26
Pacific Biosciences

## Slide 27
Pacific Biosciences

## Slide 28
Pacific Biosciences

## Slide 31
(Rhoads, Genomics Proteomics Bioinformatics, 2015)
Length of PacBio reads
2015
Half of reads > 20 kb
Top 5% of reads > 40 kb
Longest reads > 40 kb

## Slide 32
(Rhoads, Genomics Proteomics Bioinformatics, 2015)
Length of PacBio reads
Data from 35 kb size-selected E. coli library
Sequel II System ; 2.0 Chemistry
2015
Half of reads > 20 kb
Half of reads > 50 kb
2019
Top 5% of reads > 40 kb
Top 5% of reads > 135 kb
Longest reads > 40 kb
Longest reads > 175 kb

## Slide 33
Pacific Biosciences
Circular consensus sequencing (CCS) reads are obtained when the SMRT bell template is replicated several times by the polymerase
This allows a highly accurate sequencing by correction of random errors
RECENT IMPROVEMENT WITH NEW CHEMISTRY

## Slide 34
RECENT IMPROVEMENT: GENOME ASSEMBLY WITH CCS

## Slide 35
Circular consensus assembly of a human genome
Wenger et al. Nat. Biotechnol. oct. 2019
RECENT IMPROVEMENT: GENOME ASSEMBLY WITH CCS

## Slide 36
Circular consensus assembly of a human genome
Wenger et al. Nat. Biotechnol. oct. 2019
RECENT IMPROVEMENT: GENOME ASSEMBLY WITH CCS

## Slide 37
Circular consensus assembly of a human genome
Wenger et al. Nat. Biotechnol. oct. 2019
Canu assembly : genome size 3.42 Gb larger than the expected haploid human genome
because it resolves some heterozygous alleles into separate contigs
RECENT IMPROVEMENT: GENOME ASSEMBLY WITH CCS
CCS reads alone produced a contiguous and accurate genome with a concordance of 99.997%, substantially outperforming assembly with less-accurate long reads

## Slide 38
Miyamoto et al. BMC Genomics 2014
De novo assembly of Vibrio parahaemolyticus (5 Mb): two circular chromosomes
GENOME ASSEMBLY

## Slide 39
De novo Assembly of Two Swedish Genomes Reveals Missing Segments
from the Human Reference (hg38)
Ameur et al. Genes, 2018
10 Mb of the 2 genomes are absent from hg38 reference
1 Mb are assigned to chr. Y
6 Mb are shared with a Chinese personal genome
Inclusion of these sequences in GRCh38 genome radically
improves alignment and variant calling from short-read data :
re-analysis :
  yields > 75,000 putative novel single nucleotide variants (SNVs)
  removes > 10,000 false positive SNV calls per individual
PacBio GENOME ASSEMBLY
It becomes possible to represent specific population groups by assembly of representative genomes from different populations.